## Slide 1: Parallel Processing
William Stallings Computer Organization and Architecture 8th Edition

## Slide 2: Multiple Processor Organization
Single instruction, single data stream - SISD
Single instruction, multiple data stream - SIMD
Multiple instruction, single data stream - MISD
Multiple instruction, multiple data stream- MIMD

## Slide 3: Single Instruction, Single Data Stream - SISD
Single processor
Single instruction stream
Data stored in single memory
Uni-processor

## Slide 4: Single Instruction, Multiple Data Stream - SIMD
Single machine instruction
Controls simultaneous execution
Number of processing elements
Lockstep basis
Each processing element has associated data memory
Each instruction executed on different set of data by different processors
Vector and array processors

## Slide 5: Multiple Instruction, Single Data Stream - MISD
Sequence of data
Transmitted to set of processors
Each processor executes different instruction sequence
Never been implemented

## Slide 6: Multiple Instruction, Multiple Data Stream- MIMD
Set of processors
Simultaneously execute different instruction sequences
Different sets of data
SMPs, clusters and NUMA systems

## Slide 7: Taxonomy of Parallel Processor Architectures

## Slide 8: MIMD - Overview
General purpose processors
Each can process all instructions necessary
Further classified by method of processor communication

## Slide 9: Tightly Coupled - SMP
Processors share memory
Communicate via that shared memory
Symmetric Multiprocessor (SMP)
  Share single memory or pool
  Shared bus to access memory
  Memory access time to given area of memory is approximately the same for each processor

## Slide 10: Tightly Coupled - NUMA
Nonuniform memory access
Access times to different regions of memroy may differ

## Slide 11: Loosely Coupled - Clusters
Collection of independent uniprocessors or SMPs
Interconnected to form a cluster
Communication via fixed path or network connections

## Slide 12: Parallel Organizations - SISD

## Slide 13: Parallel Organizations - SIMD

## Slide 14: Parallel Organizations - MIMD Shared Memory

## Slide 15: Parallel Organizations - MIMD Distributed Memory

## Slide 16: Symmetric Multiprocessors
A stand alone computer with the following characteristics
  Two or more similar processors of comparable capacity
  Processors share same memory and I/O
  Processors are connected by a bus or other internal connection
  Memory access time is approximately the same for each processor
  All processors share access to I/O
    Either through same channels or different channels giving paths to same devices
  All processors can perform the same functions (hence symmetric)
  System controlled by integrated operating system
    providing interaction between processors
    Interaction at job, task, file and data element levels

## Slide 17: Multiprogramming and Multiprocessing

## Slide 18: SMP Advantages
Performance
  If some work can be done in parallel
Availability
  Since all processors can perform the same functions, failure of a single processor does not halt the system
Incremental growth
  User can enhance performance by adding additional processors
Scaling
  Vendors can offer range of products based on number of processors

## Slide 19: Block Diagram of Tightly Coupled Multiprocessor

## Slide 20: Organization Classification
Time shared or common bus
Multiport memory
Central control unit

## Slide 21: Time Shared Bus
Simplest form
Structure and interface similar to single processor system
Following features provided
  Addressing - distinguish modules on bus
  Arbitration - any module can be temporary master
  Time sharing - if one module has the bus, others must wait and may have to suspend
Now have multiple processors as well as multiple I/O modules

## Slide 22: Symmetric Multiprocessor Organization

## Slide 23: Time Share Bus - Advantages
Simplicity
Flexibility
Reliability

## Slide 24: Time Share Bus - Disadvantage
Performance limited by bus cycle time
Each processor should have local cache
  Reduce number of bus accesses
Leads to problems with cache coherence
  Solved in hardware - see later

## Slide 25: Operating System Issues
Simultaneous concurrent processes
Scheduling
Synchronization
Memory management
Reliability and fault tolerance

## Slide 26: A Mainframe SMP IBM zSeries
Uniprocessor with one main memory card to a high-end system with 48 processors and 8 memory cards
Dual-core processor chip
  Each includes two identical central processors (CPs)
  CISC superscalar microprocessor
  Mostly hardwired, some vertical microcode
  256-kB L1 instruction cache and a 256-kB L1 data cache
L2 cache 32 MB
  Clusters of five
  Each cluster supports eight processors and access to entire main memory space
System control element (SCE)
  Arbitrates system communication
  Maintains cache coherence
Main store control (MSC)
  Interconnect L2 caches and main memory
Memory card
  Each 32 GB, Maximum 8 , total of 256 GB
  Interconnect to MSC via synchronous memory interfaces (SMIs)
Memory bus adapter (MBA)
  Interface to I/O channels, go directly to L2 cache

## Slide 27: IBM z990 Multiprocessor Structure

## Slide 28: Cache Coherence and MESI Protocol
Problem - multiple copies of same data in different caches
Can result in an inconsistent view of memory
Write back policy can lead to inconsistency
Write through can also give problems unless caches monitor memory traffic

## Slide 29: Software Solutions
Compiler and operating system deal with problem
Overhead transferred to compile time
Design complexity transferred from hardware to software
However, software tends to make conservative decisions
  Inefficient cache utilization
Analyze code to determine safe periods for caching shared variables

## Slide 30: Hardware Solution
Cache coherence protocols
Dynamic recognition of potential problems
Run time
More efficient use of cache
Transparent to programmer
Directory protocols
Snoopy protocols

## Slide 31: Directory Protocols
Collect and maintain information about copies of data in cache
Directory stored in main memory
Requests are checked against directory
Appropriate transfers are performed
Creates central bottleneck
Effective in large scale systems with complex interconnection schemes

## Slide 32: Snoopy Protocols
Distribute cache coherence responsibility among cache controllers
Cache recognizes that a line is shared
Updates announced to other caches
Suited to bus based multiprocessor
Increases bus traffic

## Slide 33: Write Invalidate
Multiple readers, one writer
When a write is required, all other caches of the line are invalidated
Writing processor then has exclusive (cheap) access until line required by another processor
Used in Pentium II and PowerPC systems
State of every line is marked as modified, exclusive, shared or invalid
MESI

## Slide 34: Write Update
Multiple readers and writers
Updated word is distributed to all other processors
Some systems use an adaptive mixture of both solutions

## Slide 35: MESI State Transition Diagram

## Slide 36: Increasing Performance
Processor performance can be measured by the rate at which it executes instructions
MIPS rate = f * IPC
  f processor clock frequency, in MHz
  IPC is average instructions per cycle
Increase performance by increasing clock frequency and increasing instructions that complete during cycle
May be reaching limit
  Complexity
  Power consumption

## Slide 37: Multithreading and Chip Multiprocessors
Instruction stream divided into smaller streams (threads)
Executed in parallel
Wide variety of multithreading designs

## Slide 38: Definitions of Threads and Processes
Thread in multithreaded processors may or may not be same as software threads
Process:
  An instance of program running on computer
  Resource ownership
    Virtual address space to hold process image
  Scheduling/execution
  Process switch
Thread: dispatchable unit of work within process
  Includes processor context (which includes the program counter and stack pointer) and data area for stack
  Thread executes sequentially
  Interruptible: processor can turn to another thread
Thread switch
  Switching processor between threads within same process
  Typically less costly than process switch

## Slide 39: Implicit and Explicit Multithreading
All commercial processors and most experimental ones use explicit multithreading
  Concurrently execute instructions from different explicit threads
  Interleave instructions from different threads on shared pipelines or parallel execution on parallel pipelines
Implicit multithreading is concurrent execution of multiple threads extracted from single sequential program
  Implicit threads defined statically by compiler or dynamically by hardware

## Slide 40: Approaches to Explicit Multithreading
Interleaved
  Fine-grained
  Processor deals with two or more thread contexts at a time
  Switching thread at each clock cycle
  If thread is blocked it is skipped
Blocked
  Coarse-grained
  Thread executed until event causes delay
  E.g.Cache miss
  Effective on in-order processor
  Avoids pipeline stall
Simultaneous (SMT)
  Instructions simultaneously issued from multiple threads to execution units of superscalar processor
Chip multiprocessing
  Processor is replicated on a single chip
  Each processor handles separate threads

## Slide 41: Scalar Processor Approaches
Single-threaded scalar
  Simple pipeline
  No multithreading
Interleaved multithreaded scalar
  Easiest multithreading to implement
  Switch threads at each clock cycle
  Pipeline stages kept close to fully occupied
  Hardware needs to switch thread context between cycles
Blocked multithreaded scalar
  Thread executed until latency event occurs
  Would stop pipeline
  Processor switches to another thread

## Slide 42: Scalar Diagrams

## Slide 43: Multiple Instruction Issue Processors (1)
Superscalar
  No multithreading
Interleaved multithreading superscalar:
  Each cycle, as many instructions as possible issued from single thread
  Delays due to thread switches eliminated
  Number of instructions issued in cycle limited by dependencies
Blocked multithreaded superscalar
  Instructions from one thread
  Blocked multithreading used

## Slide 44: Multiple Instruction Issue Diagram (1)

## Slide 45: Multiple Instruction Issue Processors (2)
Very long instruction word (VLIW)
  E.g. IA-64
  Multiple instructions in single word
  Typically constructed by compiler
  Operations that may be executed in parallel in same word
  May pad with no-ops
Interleaved multithreading VLIW
  Similar efficiencies to interleaved multithreading on superscalar architecture
Blocked multithreaded VLIW
  Similar efficiencies to blocked multithreading on superscalar architecture

## Slide 46: Multiple Instruction Issue Diagram (2)

## Slide 47: Parallel, Simultaneous Execution of Multiple Threads
Simultaneous multithreading
  Issue multiple instructions at a time
  One thread may fill all horizontal slots
  Instructions from two or more threads may be issued
  With enough threads, can issue maximum number of instructions on each cycle
Chip multiprocessor
  Multiple processors
  Each has two-issue superscalar processor
  Each processor is assigned thread
    Can issue up to two instructions per cycle per thread

## Slide 48: Parallel Diagram

## Slide 49: Examples
Some Pentium 4
  Intel calls it hyperthreading
  SMT with support for two threads
  Single multithreaded processor, logically two processors
IBM Power5
  High-end PowerPC
  Combines chip multiprocessing with SMT
  Chip has two separate processors
  Each supporting two threads concurrently using SMT

## Slide 50: Power5 Instruction Data Flow

## Slide 51: Clusters
Alternative to SMP
High performance
High availability
Server applications
A group of interconnected whole computers
Working together as unified resource
Illusion of being one machine
Each computer called a node

## Slide 52: Cluster Benefits
Absolute scalability
Incremental scalability
High availability
Superior price/performance

## Slide 53: Cluster Configurations - Standby Server, No Shared Disk

## Slide 54: Cluster Configurations - Shared Disk

## Slide 55: Operating Systems Design Issues
Failure Management
  High availability
  Fault tolerant
  Failover
    Switching applications & data from failed system to alternative within cluster
  Failback
    Restoration of applications and data to original system
    After problem is fixed
Load balancing
  Incremental scalability
  Automatically include new computers in scheduling
  Middleware needs to recognise that processes may switch between machines

## Slide 56: Parallelizing
Single application executing in parallel on a number of machines in cluster
  Complier
    Determines at compile time which parts can be executed in parallel
    Split off for different computers
  Application
    Application written from scratch to be parallel
    Message passing to move data between nodes
    Hard to program
    Best end result
  Parametric computing
    If a problem is repeated execution of algorithm on different sets of data
    e.g. simulation using different scenarios
    Needs effective tools to organize and run

## Slide 57: Cluster Computer Architecture

## Slide 58: Cluster Middleware
Unified image to user
  Single system image
Single point of entry
Single file hierarchy
Single control point
Single virtual networking
Single memory space
Single job management system
Single user interface
Single I/O space
Single process space
Checkpointing
Process migration

## Slide 59: Blade Servers
Common implementation of cluster
Server houses multiple server modules (blades) in single chassis
  Save space
  Improve system management
  Chassis provides power supply
  Each blade has processor, memory, disk

## Slide 60: Example 100-Gbps Ethernet Configuration for Massive Blade Server Site

## Slide 61: Cluster v. SMP
Both provide multiprocessor support to high demand applications.
Both available commercially
  SMP for longer
SMP:
  Easier to manage and control
  Closer to single processor systems
    Scheduling is main difference
    Less physical space
    Lower power consumption
Clustering:
  Superior incremental & absolute scalability
  Superior availability
    Redundancy

## Slide 62: Nonuniform Memory Access (NUMA)
Alternative to SMP & clustering
Uniform memory access
  All processors have access to all parts of memory
    Using load & store
  Access time to all regions of memory is the same
  Access time to memory for different processors same
  As used by SMP
Nonuniform memory access
  All processors have access to all parts of memory
    Using load & store
  Access time of processor differs depending on region of memory
  Different processors access different regions of memory at different speeds
Cache coherent NUMA
  Cache coherence is maintained among the caches of the various processors
  Significantly different from SMP and clusters

## Slide 63: Motivation
SMP has practical limit to number of processors
  Bus traffic limits to between 16 and 64 processors
In clusters each node has own memory
  Apps do not see large global memory
  Coherence maintained by software not hardware
NUMA retains SMP flavour while giving large scale multiprocessing
  e.g. Silicon Graphics Origin NUMA 1024 MIPS R10000 processors
Objective is to maintain transparent system wide memory while permitting multiprocessor nodes, each with own bus or internal interconnection system

## Slide 64: CC-NUMA Organization

## Slide 65: CC-NUMA Operation
Each processor has own L1 and L2 cache
Each node has own main memory
Nodes connected by some networking facility
Each processor sees single addressable memory space
Memory request order:
  L1 cache (local to processor)
  L2 cache (local to processor)
  Main memory (local to node)
  Remote memory
    Delivered to requesting (local to processor) cache
Automatic and transparent

## Slide 66: Memory Access Sequence
Each node maintains directory of location of portions of memory and cache status
e.g. node 2 processor 3 (P2-3) requests location 798 which is in memory of node 1
  P2-3 issues read request on snoopy bus of node 2
  Directory on node 2 recognises location is on node 1
  Node 2 directory requests node 1’s directory
  Node 1 directory requests contents of 798
  Node 1 memory puts data on (node 1 local) bus
  Node 1 directory gets data from (node 1 local) bus
  Data transferred to node 2’s directory
  Node 2 directory puts data on (node 2 local) bus
  Data picked up, put in P2-3’s cache and delivered to processor

## Slide 67: Cache Coherence
Node 1 directory keeps note that node 2 has copy of data
If data modified in cache, this is broadcast to other nodes
Local directories monitor and purge local cache if necessary
Local directory monitors changes to local data in remote caches and marks memory invalid until writeback
Local directory forces writeback if memory location requested by another processor

## Slide 68: NUMA Pros & Cons
Effective performance at higher levels of parallelism than SMP
No major software changes
Performance can breakdown if too much access to remote memory
  Can be avoided by:
    L1 & L2 cache design reducing all memory access
      Need good temporal locality of software
    Good spatial locality of software
    Virtual memory management moving pages to nodes that are using them most
Not transparent
  Page allocation, process allocation and load balancing changes needed
Availability?

## Slide 69: Vector Computation
Maths problems involving physical processes present different difficulties for computation
  Aerodynamics, seismology, meteorology
  Continuous field simulation
High precision
Repeated floating point calculations on large arrays of numbers
Supercomputers handle these types of problem
  Hundreds of millions of flops
  $10-15 million
  Optimised for calculation rather than multitasking and I/O
  Limited market
    Research, government agencies, meteorology
Array processor
  Alternative to supercomputer
  Configured as peripherals to mainframe & mini
  Just run vector portion of problems

## Slide 70: Vector Addition Example

## Slide 71: Approaches
General purpose computers rely on iteration to do vector calculations
In example this needs six calculations
Vector processing
  Assume possible to operate on one-dimensional vector of data
  All elements in a particular row can be calculated in parallel
Parallel processing
  Independent processors functioning in parallel
  Use FORK N to start individual process at location N
  JOIN N causes N independent processes to join and merge following JOIN
    O/S Co-ordinates JOINs
    Execution is blocked until all N processes have reached JOIN

## Slide 72: Processor Designs
Pipelined ALU
  Within operations
  Across operations
Parallel ALUs
Parallel processors

## Slide 73: Approaches to Vector Computation

## Slide 74: Chaining
Cray Supercomputers
Vector operation may start as soon as first element of operand vector available and functional unit is free
Result from one functional unit is fed immediately into another
If vector registers used, intermediate results do not have to be stored in memory

## Slide 75: Computer Organizations

## Slide 76: IBM 3090 with Vector Facility