## Slide 1: William Stallings Computer Organization and Architecture 8th Edition
Chapter 15
Control Unit Operation

## Slide 2: Micro-Operations
A computer executes a program
Fetch/execute cycle
Each cycle has a number of steps
  see pipelining
Called micro-operations
Each step does very little
Atomic operation of CPU

## Slide 3: Constituent Elements of Program Execution

## Slide 4: Fetch - 4 Registers
Memory Address Register (MAR)
  Connected to address bus
  Specifies address for read or write op
Memory Buffer Register (MBR)
  Connected to data bus
  Holds data to write or last data read
Program Counter (PC)
  Holds address of next instruction to be fetched
Instruction Register (IR)
  Holds last instruction fetched

## Slide 5: Fetch Sequence
Address of next instruction is in PC
Address (MAR) is placed on address bus
Control unit issues READ command
Result (data from memory) appears on data bus
Data from data bus copied into MBR
PC incremented by 1 (in parallel with data fetch from memory)
Data (instruction) moved from MBR to IR
MBR is now free for further data fetches

## Slide 6: Fetch Sequence (symbolic)
t1: MAR <- (PC)
t2: MBR <- (memory)
PC <- (PC) +1
t3: IR <- (MBR)
(tx = time unit/clock cycle)
or
t1: MAR <- (PC)
t2: MBR <- (memory)
t3: PC <- (PC) +1
IR <- (MBR)

## Slide 7: Rules for Clock Cycle Grouping
Proper sequence must be followed
  MAR <- (PC) must precede MBR <- (memory)
Conflicts must be avoided
  Must not read & write same register at same time
  MBR <- (memory) & IR <- (MBR) must not be in same cycle
Also: PC <- (PC) +1 involves addition
  Use ALU
  May need additional micro-operations

## Slide 8: Indirect Cycle
MAR <- (IRaddress) - address field of IR
MBR <- (memory)
IRaddress <- (MBRaddress)
MBR contains an address
IR is now in same state as if direct addressing had been used
(What does this say about IR size?)

## Slide 9: Interrupt Cycle
t1: MBR <-(PC)
t2: MAR <- save-address
PC <- routine-address
t3: memory <- (MBR)
This is a minimum
  May be additional micro-ops to get addresses
  N.B. saving context is done by interrupt handler routine, not micro-ops

## Slide 10: Execute Cycle (ADD)
Different for each instruction
e.g. ADD R1,X - add the contents of location X to Register 1 , result in R1
t1: MAR <- (IRaddress)
t2: MBR <- (memory)
t3: R1 <- R1 + (MBR)
Note no overlap of micro-operations

## Slide 11: Execute Cycle (ISZ)
ISZ X - increment and skip if zero
  t1: MAR <- (IRaddress)
  t2: MBR <- (memory)
  t3: MBR <- (MBR) + 1
  t4: memory <- (MBR)
  if (MBR) == 0 then PC <- (PC) + 1
Notes:
  if is a single micro-operation
  Micro-operations done during t4

## Slide 12: Execute Cycle (BSA)
BSA X - Branch and save address
  Address of instruction following BSA is saved in X
  Execution continues from X+1
  t1: MAR <- (IRaddress)
  MBR <- (PC)
  t2: PC <- (IRaddress)
  memory <- (MBR)
  t3: PC <- (PC) + 1

## Slide 13: Instruction Cycle
Each phase decomposed into sequence of elementary micro-operations
E.g. fetch, indirect, and interrupt cycles
Execute cycle
  One sequence of micro-operations for each opcode
Need to tie sequences together
Assume new 2-bit register
  Instruction cycle code (ICC) designates which part of cycle processor is in
    00: Fetch
    01: Indirect
    10: Execute
    11: Interrupt

## Slide 14: Flowchart for Instruction Cycle

## Slide 15: Functional Requirements
Define basic elements of processor
Describe micro-operations processor performs
Determine functions control unit must perform

## Slide 16: Basic Elements of Processor
ALU
Registers
Internal data pahs
External data paths
Control Unit

## Slide 17: Types of Micro-operation
Transfer data between registers
Transfer data from register to external
Transfer data from external to register
Perform arithmetic or logical ops

## Slide 18: Functions of Control Unit
Sequencing
  Causing the CPU to step through a series of micro-operations
Execution
  Causing the performance of each micro-op
This is done using Control Signals

## Slide 19: Control Signals
Clock
  One micro-instruction (or set of parallel micro-instructions) per clock cycle
Instruction register
  Op-code for current instruction
  Determines which micro-instructions are performed
Flags
  State of CPU
  Results of previous operations
From control bus
  Interrupts
  Acknowledgements

## Slide 20: Model of Control Unit

## Slide 21: Control Signals - output
Within CPU
  Cause data movement
  Activate specific functions
Via control bus
  To memory
  To I/O modules

## Slide 22: Example Control Signal Sequence - Fetch
MAR <- (PC)
  Control unit activates signal to open gates between PC and MAR
MBR <- (memory)
  Open gates between MAR and address bus
  Memory read control signal
  Open gates between data bus and MBR

## Slide 23: Data Paths and Control Signals

## Slide 24: Internal Organization
Usually a single internal bus
Gates control movement of data onto and off the bus
Control signals control data transfer to and from external systems bus
Temporary registers needed for proper operation of ALU

## Slide 25: CPU with Internal Bus

## Slide 26: Intel 8085 CPU Block Diagram

## Slide 27: Intel 8085 Pin Configuration

## Slide 28: Intel 8085 OUT Instruction Timing Diagram

## Slide 29: Hardwired Implementation (1)
Control unit inputs
Flags and control bus
  Each bit means something
Instruction register
  Op-code causes different control signals for each different instruction
  Unique logic for each op-code
  Decoder takes encoded input and produces single output
  n binary inputs and 2n outputs

## Slide 30: Hardwired Implementation (2)
Clock
  Repetitive sequence of pulses
  Useful for measuring duration of micro-ops
  Must be long enough to allow signal propagation
  Different control signals at different times within instruction cycle
  Need a counter with different control signals for t1, t2 etc.

## Slide 31: Control Unit with Decoded Inputs

## Slide 32: Problems With Hard Wired Designs
Complex sequencing & micro-operation logic
Difficult to design and test
Inflexible design
Difficult to add new instructions

## Slide 33: Required Reading
Stallings chapter 15