## Slide 1: William Stallings Computer Organization and Architecture 8th Edition
Chapter 16
Micro-programmed Control

## Slide 2: Control Unit Organization

## Slide 3: Micro-programmed Control
Use sequences of instructions (see earlier notes) to control complex operations
Called micro-programming or firmware

## Slide 4: Implementation (1)
All the control unit does is generate a set of control signals
Each control signal is on or off
Represent each control signal by a bit
Have a control word for each micro-operation
Have a sequence of control words for each machine code instruction
Add an address to specify the next micro-instruction, depending on conditions

## Slide 5: Implementation (2)
Today’s large microprocessor
  Many instructions and associated register-level hardware
  Many control points to be manipulated
This results in control memory that
  Contains a large number of words
    co-responding to the number of instructions to be executed
  Has a wide word width
    Due to the large number of control points to be manipulated

## Slide 6: Micro-program Word Length
Based on 3 factors
  Maximum number of simultaneous micro-operations supported
  The way control information is represented or encoded
  The way in which the next micro-instruction address is specified

## Slide 7: Micro-instruction Types
Each micro-instruction specifies single (or few) micro-operations to be performed
  (vertical micro-programming)
Each micro-instruction specifies many different micro-operations to be performed in parallel
  (horizontal micro-programming)

## Slide 8: Vertical Micro-programming
Width is narrow
n control signals encoded into log2 n bits
Limited ability to express parallelism
Considerable encoding of control information requires external memory word decoder to identify the exact control line being manipulated

## Slide 9: Horizontal Micro-programming
Wide memory word
High degree of parallel operations possible
Little encoding of control information

## Slide 10: Typical Microinstruction Formats

## Slide 11: Compromise
Divide control signals into disjoint groups
Implement each group as separate field in memory word
Supports reasonable levels of parallelism without too much complexity

## Slide 12: Organization of Control Memory

## Slide 13: Control Unit

## Slide 14: Control Unit Function
Sequence login unit issues read command
Word specified in control address register is read into control buffer register
Control buffer register contents generates control signals and next address information
Sequence login loads new address into control buffer register based on next address information from control buffer register and ALU flags

## Slide 15: Next Address Decision
Depending on ALU flags and control buffer register
  Get next instruction
    Add 1 to control address register
  Jump to new routine based on jump microinstruction
    Load address field of control buffer register into control address register
  Jump to machine instruction routine
    Load control address register based on opcode in IR

## Slide 16: Functioning of Microprogrammed Control Unit

## Slide 17: Wilkes Control
1951
Matrix partially filled with diodes
During cycle, one row activated
  Generates signals where diode present
  First part of row generates control
  Second generates address for next cycle

## Slide 18: Wilkes's Microprogrammed Control Unit

## Slide 19: Advantages and Disadvantages of Microprogramming
Simplifies design of control unit
  Cheaper
  Less error-prone
Slower

## Slide 20: Tasks Done By Microprogrammed Control Unit
Microinstruction sequencing
Microinstruction execution
Must consider both together

## Slide 21: Design Considerations
Size of microinstructions
Address generation time
  Determined by instruction register
    Once per cycle, after instruction is fetched
  Next sequential address
    Common in most designed
  Branches
    Both conditional and unconditional

## Slide 22: Sequencing Techniques
Based on current microinstruction, condition flags, contents of IR, control memory address must be generated
Based on format of address information
  Two address fields
  Single address field
  Variable format

## Slide 23: Branch Control Logic: Two Address Fields

## Slide 24: Branch Control Logic: Single Address Field

## Slide 25: Branch Control Logic: Variable Format

## Slide 26: Address Generation
Explicit | Implicit
Two-field | Mapping
Unconditional Branch | Addition
Conditional branch | Residual control

## Slide 27: Execution
The cycle is the basic event
Each cycle is made up of two events
  Fetch
    Determined by generation of microinstruction address
  Execute

## Slide 28: Execute
Effect is to generate control signals
Some control points internal to processor
Rest go to external control bus or other interface

## Slide 29: Control Unit Organization

## Slide 30: A Taxonomy of Microinstructions
Vertical/horizontal
Packed/unpacked
Hard/soft microprogramming
Direct/indirect encoding

## Slide 31: Required Reading
Stallings chapter 21